## Slide 1: Liquid level recognition

## Slide 2: Content
Problem
Dataset
Pixel Per Metric (PPM)
Camera calibration
Final results

## Slide 3: The problem we aimed to tackle is the accurate measurement of liquid height in a transparent glass, based only on an image.
3
Problem
Notes: Problem
non-intrusive method concept

## Slide 4: Dataset
Notes: X – Y letters
Consistent Camera Angles
Uniform Lighting Conditions
Neutral Background Selection
Multiple Liquid Types for Robustness
Consistent Distance and Framing (for PPM)

## Slide 5: Idea
To address this challenge, we leveraged the known dimension, that is the height of the glass, in order to use it as a reference object and establish a pixels per metric (PPM) ratio.

## Slide 6: Workflow
Apply Gaussian filter
Glass handling:
  Detect glass edges
  Detect glass contours
Reduce the area of the image to handle liquid
  Detect liquid edges
  Detect liquid contours
Apply PPM

## Slide 7: improvements
Camera calibration
Noise reduction and background filtering

## Slide 8: CAMERA CALIBRATION
Camera calibration consists in estimating all the necessary intrinsic and extrinsic parameters required to avoid distortion in the captured images.
Intrinsic parameters:
Focal length
Optical center
Radial and tangential distortion coefficients of the lens
Extrinsic parameters:
Rotation matrix R
Translation vector t

## Slide 9: Method used
To accurately calibrate the camera, we capture multiple images of the checkerboard pattern from different viewpoints.
The camera remains stationary, while the checkerboard is moved to different orientations.

## Slide 10: Noise reduction and background filtering
We applied more preprocessing techniques to improve our result:
Thresholding (Otsu’s Method) Converts the image into a binary mask.
Morphological Operations Helps refine the object’s contour.
Adaptive Thresholding Useful for varying lighting conditions
Notes: Otsu’s method (intra-class)
Morphological (OPEN, CLOSE)
Adaptive (Percentile)

## Slide 11: Before - after

## Slide 12: Thanks Q&A
Donald Gera
Alessandro Moscatelli